## Slide 1
Deployment-Oriented Neural Network State Estimation for Battery Management Systems
Florian Rzepka | Technische Universität Berlin | 2026
Seite 1
Florian Rzepka | Doctoral Defense | 2026

## Slide 2
Motivation and research questions
Evaluation framework and experimental basis
Compact neural ageing estimation
Robustness benchmarking
Embedded AI and model compression
Integrated findings and outlook
Structure
Seite 2
Florian Rzepka | Doctoral Defense | 2026

## Slide 3
Motivation and Research Questions
Seite 3
Florian Rzepka | Doctoral Defense | 2026

## Slide 4
Why Deployment-Oriented State Estimation?
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
• SOC and SOH as non-measurable internal battery states
• Field signals with bias, noise, missing data, and timing irregularities
• Embedded limits in flash, RAM, latency, and energy
• Accuracy alone as an incomplete deployment criterion
One estimator path
Data representation to MCU execution
Seite 4
Florian Rzepka | Doctoral Defense | 2026

## Slide 5
Research Questions and Contribution Path
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
1
Representation
Ageing-relevant history in compact neural estimators
2
Robustness
Matched disturbances across estimator families
3
Deployment
Compression, firmware transfer, and MCU measurement
• RQ1: Which input representation captures battery ageing?
• RQ2: Which estimator remains reliable under disturbed measurements?
• RQ3: Which compression route preserves accuracy within embedded limits?
Seite 5
Florian Rzepka | Doctoral Defense | 2026

## Slide 6
Evaluation Framework and Experimental Basis
Seite 6
Florian Rzepka | Doctoral Defense | 2026

## Slide 7
Three Coupled BMS Requirement Dimensions
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
Joint evaluation
• Performance: accuracy, recovery, disturbance response
• Hardware: flash, RAM, latency, energy
• Deployment: features, export, firmware, repeatability
3 dimensions
No single metric as a substitute
Seite 7
Florian Rzepka | Doctoral Defense | 2026

## Slide 8
Estimator Families and Evaluation Logic
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
• Direct-measurement: low complexity, accumulated drift
• Model-based and hybrid: physical correction paths
• Data-driven: flexible nonlinear mapping and temporal context
• Matched assessment: baseline, disturbance sensitivity, recovery
Seite 8
Florian Rzepka | Doctoral Defense | 2026

## Slide 9
Experimental Basis and Embedded Execution Chain
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
NMC ageing study
• 14 cells
• 7 ageing scenarios
• Capacity-based SOH labels
LFP DoE campaign
• 15 cells
• 8 operating points
• 1 Hz measurement stream
Embedded chain
• Custom 4s BMS platform
• STM32H7 execution
• Common sensing and firmware basis
Seite 9
Florian Rzepka | Doctoral Defense | 2026

## Slide 10
Compact Neural Ageing Estimation
Seite 10
Florian Rzepka | Doctoral Defense | 2026

## Slide 11
Time-Aware Features for a Feedforward Model
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
Engineered temporal context
• Voltage, current, and temperature measurements
• Cumulative-current throughput features
• 16 lag steps at 10 min resolution
• 160 min effective history
Seite 11
Florian Rzepka | Doctoral Defense | 2026

## Slide 12
Compact MLP Architecture for SOH Estimation
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
• Compact feedforward architecture
• Time dependence encoded in engineered inputs
• SOH output from operational measurements
• Low architectural complexity
Seite 12
Florian Rzepka | Doctoral Defense | 2026

## Slide 13
Ageing-Estimation Results
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
1.10 pp
Average SOH MAE
16 x 10 min
Best lag configuration
Cell 9
Reduced transfer to atypical ageing
Seite 13
Florian Rzepka | Doctoral Defense | 2026

## Slide 14
Robustness Benchmarking
Seite 14
Florian Rzepka | Doctoral Defense | 2026

## Slide 15
Matched Benchmark Across Four Estimator Classes
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
• DM: direct Coulomb-counting path
• HDM: direct path with shared SOH context
• HECM: equivalent-circuit observer with SOH context
• DD: recurrent data-driven SOC estimator
• Identical online stream and matched disturbance protocols
Seite 15
Florian Rzepka | Doctoral Defense | 2026

## Slide 16
Clean Accuracy Is Only the Starting Point
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
0.24 pp
HDM baseline MAE
0.90 pp
HECM baseline MAE
1.00 pp
DD baseline MAE
3.11 pp
DM baseline MAE
Seite 16
Florian Rzepka | Doctoral Defense | 2026

## Slide 17
Disturbances Change the Estimator Ranking
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
• Current bias: HECM strongest
• Missing samples: DD strongest
• Initialization mismatch: DD fastest strict recovery
• Noise and spikes: estimator-specific propagation paths
Ranking shift
Fault type as decisive context
Seite 17
Florian Rzepka | Doctoral Defense | 2026

## Slide 18
Robustness Result: No Universal Winner
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
Selection target: acceptable accuracy, recovery, and disturbance response for the intended operating profile
Seite 18
Florian Rzepka | Doctoral Defense | 2026

## Slide 19
Embedded AI and Model Compression
Seite 19
Florian Rzepka | Doctoral Defense | 2026

## Slide 20
Stateful Estimation from Training to STM32
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
Stateful 1 Hz replay | Explicit recurrent states | PyTorch-to-C export | STM32 measurements
Seite 20
Florian Rzepka | Doctoral Defense | 2026

## Slide 21
Two Compression Routes
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
Structured pruning
• 30% hidden-channel reduction
• Smaller dense tensors
• Post-pruning fine-tuning
INT8 weight quantization
• Row-wise signed symmetric mapping
• Recurrent weights in INT8
• Scales, states, and MLP in FP32
Seite 21
Florian Rzepka | Doctoral Defense | 2026

## Slide 22
Accuracy and Long-Horizon Stability
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
SOC streaming replay
SOH streaming replay
• SOC MAE: 2.68 / 2.34 / 2.79 pp
• SOH MAE: 0.85 / 1.46 / 1.41 pp
• Order: Base / Pruned / Quantized
• No increasing Quantized-to-Base divergence
Seite 22
Florian Rzepka | Doctoral Defense | 2026

## Slide 23
Resource, Latency, and Utility Trade-Offs
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
SOC operating points
• Pruned: -41% flash, -43% kernel time
• Quantized: -50% flash, +399% kernel time
• Utility: 0.71 Pruned / 1.83 Quantized
SOH operating points
• Pruned: -46% flash, -44% kernel time
• Quantized: -59% flash, +29% kernel time
• Constraint-dependent optimum
Seite 23
Florian Rzepka | Doctoral Defense | 2026

## Slide 24
Integrated Findings and Outlook
Seite 24
Florian Rzepka | Doctoral Defense | 2026

## Slide 25
Integrated Findings Across the Three Studies
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
1
Representation
Cumulative-current and lag features enable compact ageing estimation
2
Validation
Nominal accuracy, recovery, and disturbances require separate evidence
3
Implementation
Compression choice depends on the active hardware constraint
• Model class alone does not determine deployment suitability
• Feature pipeline, estimator, compression, firmware, and hardware as one design system
• Transferable evaluation logic instead of one universal estimator ranking
Seite 25
Florian Rzepka | Doctoral Defense | 2026

## Slide 26
Design Rules, Limitations, and Outlook
1. Motivation
2. Framework
3. Ageing
4. Robustness
5. Embedded AI
6. Synthesis
Design rules
• Representative features before model complexity
• Disturbance testing beyond clean MAE
• Compression matched to flash, RAM, or latency bottleneck
• Target-hardware validation before deployment
Next steps
• Additional cells, chemistries, and operating profiles
• Live disturbance injection in firmware and sensing chain
• Joint pruning and quantization
• Larger packs and longer autonomous operation
Main conclusion
Deployment readiness as a system property
Seite 26
Florian Rzepka | Doctoral Defense | 2026

## Slide 27
Thank You | Questions
Seite 27
Florian Rzepka | Doctoral Defense | 2026